## Slide 1: Grevol VCU

## Slide 2
Microcontroller
stm32g0b1cet6
Serial Flash
w25q512
SPI
CAN Bus
UART
Analog In
Digital In
Digital Out
PWM Out*
Freq In*
Cell Monitoring Board 1
Cell Monitoring Board 2
Cell Monitoring Board 3
Cell Monitoring Board 4
VCU
MCU
Instrument Cluster
Telematics

## Slide 3
Analog Inputs
  Throttle
  Leakage
  Supply Current
  Charge current
  Discharge current
  Supply voltage
  Dcdc converter voltage
  Load Voltage
  DC bus voltage
Digital Inputs
  Brake
  Charger connection
  Parking
  Ignition
Digital Outputs
  Alarm
  Clutch
  Gear

## Slide 4
pc13 | Pre
pa0 | Vbs
pa1 | Vls
Pb1 | Fire
Pb12 | Dcon
Pb13 | Sdr1
Pb14 | Son
Pb15 | Adio
Pa9/pa10 | Uart
Pc6 | Brkre
Pa11 | Cont
Pa12 | Dirc
Pa13 | Ing
Pa14 | Brak
Pa15 | Tac
Pd0/pd1 | Can
Pd2 | Clut
Pd3 | Nss
Pb6 | Trc
Pb7 | Mode
Pa2 | Disi – curr sense
Pa3 | Ci – curr sense
Pb0/pb2 | Ad9/ad10 – LEAKAGE
Pa5 | AD7 – supply curr sense
Pa4 | Ad5- throttle
Pa5 | Ad6-dcdc voltage
Pa7 | Ad8-supply voltage

## Slide 5
UC Pin | Signal | Type
PA14 | Brak- brake pressed | GPIn
PA13 | Ing – ignition in | GPIn
PA12 | Dirc – drive direction | GPIn
PA11 | Cont-contactor out | GPOut
PA10 | Urx – uart rx | UART RX
PC7 | Park – parking in | GPIn
PC6 | brkre – braking resistor out | GPOut
PA9 | Utx – uart tx | UART TX
PA8 | F3-fan 3 out | GPOut
PB15 | Adio-buzzer out pwm | PWM Out
PB14 | Son-24W supply ctrl | GPOut
PB13 | Sdr1-7W supply ctrl | GPOut
UC Pin | Signal | Type
PB12 | Dcon – DC-DC ON | GPOut
PB11 | Gr01 – gear out1 | GPOut
PB10 | Gr02 - gear out 2 | GPOut
PB2 | AD10 – leakage LL | ADC In
PB1 | Fire – fire alarm | GPOut
PB0 | AD9 – leakage HL | ADC In
PA7 | AD8 – 12v supply v sense | ADC In
PA6 | AD7 – batt internal current – 20A max | ADC In
PA5 | AD6 – dcdc con out | ADC In
PA4 | Ad5 – throttle in | ADC In
PA3 | Ci – charging current (400A) | ADC In
PA2 | Disi – discharging curr (400A) | ADC In

## Slide 6
UC Pin | Signal | Type
PC13 | Pre- precharge out | GP out
PC14 | OSCIn 32khz | 
PC15 | OSCou 32khz | 
VBAT |  | 
VRE |  | 
VDD |  | 
VSS |  | 
PF0 | F1- fan 1 out | GPOut
PF1 | F2 – fan2 out | GPOut
PF2 | nrst | 
PA0 | Vbs-batt v before contactor(77.5V) | ADC In
PA1 | Vls-battv after contactor | ADC In
UC Pin | Signal | Type
PB9 | Grin2 – gear in? | GPIn
PB8 | Grin1 – gear in? | GPIn
PB7 | Mode- fwd-rev | GPIn
PB6 | TRC – PWMOut Throttle | PWM Out
PB5 | MOSI- SFLASH | SPI
PB4 | MISO- SFLASH | SPI
PB3 | SCK- SFLASH | SPI
PD3 | NSS – SFLASH | GPOut
PD2 | Clutch out | GPOut
PD1 | FDCTX– CAN | CAN
PD0 | FDCRX-CAN | CAN
PA15 | TAC – speed in/ Freq In | Freq In

## Slide 7
MODULES
  Battery Management
    UART Communication with Battery monitor
    SOC
    DCL-CCL
    SOH
    Supervisory and Faults
    Charger Interface
    DC-DC monitoring
  VCU
    Vehicle Control (Tq demand to MCU)
    ODO tracking
    Supervisory and Faults
    UART/CAN communication with IoT
    Auto Gear control
    RTC
    Throttle override*
  Telematics
    Data Tx to server
    Data Rx from server
  Device Driver Interface
    CAN - Done
    UART - Done
    SPI (S-Flash) - Done
    ADC - Done
    DIO – Done
    Freq In
    PWM Out - Done

## Slide 8
Battery Management State Machine
INIT/POST
CHARGING
DRIVE
FAULT RESET
FAULT LATCH
IMMOBILIZE
DEEP DISCHARGE
FAULT
IDLE
SLEEP
Fault
Charge
Detect
Fault
Fault Clear
> 3 times within
1 min
< 3 times within
1 min
CellV too Low
Ignition
detect
Immobilize
signal
Fault
Fault
Power Cycle
timeout
Ignition/charge detect

## Slide 9
Charging Sub-Modes
IDLE
Charger CAN received
Charging CC
Charging CV
End Of Charging
Batt V > xV OR Cell V > xV
Batt V > xV AND Curr < 10A OR Cell V > xV
Charger CAN timeout
Charger CAN timeout

## Slide 10
VCU State Machine
INIT/POST
DRIVE
FAULT RESET
FAULT LATCH
FAULT
IDLE
SLEEP
Fault
Fault
Fault Clear
> 3 times within
1 min
< 3 times within
1 min
Fault
Power Cycle
timeout
PRECHARGE
CONTACTOR
Ignition
Ignition/charge detect

## Slide 11
Drive Modes
Neutral/Idle
Reverse
ECO
BOOST
Limp Home
Immobilize
Ignitin On
Mode ECO AND
Dir FWD
Speed 0 AND
Dir REV
Mode Boost AND
Dir FWD
SOC < 15% OR
DCL < 100A
FAULT action Limp Home OR
Thermal Warning
Park detected OR
CAHRGER detected OR
Immobilize Request

## Slide 12
SW Architecture
Driver DB
VCU DB
BMS DB
CAN Comm Process
UART Comm Process
SPI Comm Process
SFlash
VCU Process
BMS Process
Analog Process
GPIO Process
PWM & FrqIn Process
Telematics Process

## Slide 13
HAL
Driver Abstraction
BMS
VCU
SW Architecture
BMS Processes | Exec Rate
BMS_comm_process | 500 ms
BMS_soc_soh_process | 500 ms
BMS_current_limit_process | 500 ms
BMS_supervisory_process | 100 ms
BMS_fault_monitor_process | 100 ms
BMS_charger_comm_process | 100 ms
Driver Processes | Exec Rate
DRV_digitalIO_process | 10 ms
DRV_analogio_process | 10 ms
DRV_uart_RX_intr | Interrupt
DRV_can_RX_intr | Interrupt
DRV_sflash_process | 1 min
VCU Processes | Exec Rate
VCU_vehicle_control_process | 100 ms
VCU_mcu_comm_process | 100 ms
VCU_supervisory_process | 100 ms
VCU_fault_monitor_process | 100 ms
VCU_telematics_comm | 10 sec

## Slide 14
Inputs Analog Signals
 Thro􀆩le Demand
 Current (Ba􀆩ery)
 Load Voltage
 Ba􀆩ery Voltage
 DC -DC Voltage
 DC-DC current
 BOX open signal
 Local Supply Current
Input Digital Signal
 Speed
 Gear 1
 Gear 2
 ECO / Boost
 Forward / Reverse
 Clutch
 Brake
 Brake Fluid
 Igni􀆟on
 Park
Output Signal From VCU
 Thro􀆩le
 Signal Supply ON
 Gear 1 Change
 Gear 2 Change
 Neutral
 Brake Resistor
 Fire Alarm
 Pre-Charge ON
 Contactor ON
 Cooling Fan 1 ON
 Cooling Fan 2 ON
 Fan 3 ON
 DC -DC Unit/Board
 UART
 CAN (Bus bi-direc􀆟onal) (Input and output through can line and how to generate)
 USB
 Internal SPI
 Leakage detec􀆟on (Only if double pole contactor or two relays are used)
 Brake Fluid Low Signal to be provided (Digital Out) to have an indica􀆟on to driver and to have a
no􀆟fica􀆟on to the server.

## Slide 15
TO-DO : Mapping of the hardware IOs with chip pins

## Slide 16
List of Faults
  BMS
    Cell OV 1
    Cell OV 2
    Cell UV
    Pack OV
    Pack UV
    Charge Over Current
    Discharge Over Current
    Battery Over Voltage
    Battery Under Voltage
    Over Temp
    Under Temp
    BMS Comm Fault
    Current Sensor Fault
    Thermal Runaway
    Unauthorized charger fault
    Electrical Leakage fault
    Contactor Fault
    Cell Imbalance Warning
    Open Wire Fault
    Partial Charge Warning
    Thermistor Warning/Disable
  List of Faults
    VCU
      Precharge Fault
      Input Voltage Fault
      Controller Fault
      DC-DC Fault
      Aux OC fault
      Brake Fluid Low Fault
      Throttle sense Fault
      Brake sense Fault
      BMS comm Fault
      MCU Fault
      MCU comm Fault
      Brake resistor Fault
      Over load fault
      Speed sense fault/Over speed fault

## Slide 17
Decision making for VCU,HW/fw/system
Fault | Reason/Condition | Action/Decision | Remarks